Clarification No 1 and Corrigendum No 2 to the tender dossier: Works on adaptation of the construction of the Pump Station Duklo in the Municipality of Niksic

EuropeAid/131194/L/ACT/ME – CRIS No: 2011/274-410-TD/004

ANSWERS ON THE QUESTIONS FROM THE SITE VISIT

| TENDERERS' QUESTIONS | CONTRACT AUTHORITY'S RESPONSES |
| --- | --- |
| What is the estimated value of the works? | when it's about procurement of works, in accordance with EU regulations and procedures already defined in PRAG, we are not allowed to announce the estimated value of tender. |
| Is there any substation? Did you foreseen it's reconstruction? | There is a power station, but its reconstruction is not foreseen in this tender. |
| What is included in the project? | Replacement of existing roof construction, replacement of locks, replacement of floor and wall ceramic sanitary, replacing wiring and lighting, construction of electrostatics floor, inner paintworks (Please refer to the Bill of Quantities) |
| Is there provided a backup power of the facility? | A backup power of the facility is not provided. |
| Is it in the Bill ROOF COVERING, POS100- unit measures m2 or m3? | Unit of measure for roofing is m2. In Volume 4 was mistakenly written m3. |
| Is it necessary to submit certificate Attesting for the materials offered, within the tender documents? | It is not required to submit certificates of quality building material in the technical documentation. Submission of certificate of quality has to be done after construction to commissioning as defined under the national law. |
| For which three years should be submitted financial reports and the like? | The average annual turnover in construction works of the tenderer in the past 3 years must be at least EUR 1.500.000,00 (one million five hundred thousand Euro). The last three years are the years for which you have completed your financial reports. Most probably 2012, 2011 and 2010 or 2011, 2010 and 2009. |

REVIEW OF STANDARDS

These standards integrates and supplements the standards included in the Volume 3 of the tender dossier. Tenderers are informed that any material indicated in the Bill of Quantity will have to respect at least either the European Standards or the National standards.

| REVIEW OF STANDARDS FOR WINDOWS AND EXTERIOR DOORS |
| --- |
| TECHNICAL REQUIREMENTS | EUROPEAN STANDARDS | NATIONAL STANDARDS |
|  | TESTING METHOD | CLASSIFICATION | TESTING METHOD | CLASSIFICATION |
| Thermal isolation | EN 10077 |  |  |  |
| Water leaks | EN 1027 | EN 12208 | MEST EN 1027:2009 | MEST EN 12208:2009 |
| Air leaks | EN 1026 | EN 12207 | MEST EN 1026:2009 | MEST EN 12207:2009 |
| Loads from wind | EN 12211 | EN 12210 | MEST EN 12211:2009 | MEST EN 12210:2009 |
| Soundproofing | EN 717 EN 20140 |  |  |  |
| Mechanical characteristics | vertical load and lateral buckling | EN 948-1 | EN 13115 |  | MEST EN 13115:2009 |
|  | permanence and orderly functioning | EN 1191 | EN 12400 | MEST EN 1191:2009 | MEST EN 12400:2009 |
|  | Resistance to shock | EN 13049 | EN 13049 | MEST EN 13049:2009 | MEST EN 13049:2009 |
| Light transmittance | EN 410 |  | MEST EN 410:2011 |  |
| Security against burglary |  | EN 1627 |  | MEST EN 1627:2012 |
| REVIEW OF STANDARDS FOR INTERIOR DOORS |
| TECHNICAL REQUIREMENTS | EUROPEAN STANDARDS | NATIONAL STANDARDS |
|  | TESTING METHOD | CLASSIFICATION | TESTING METHOD | CLASSIFICATION |
| Dimensions of wings | EN 951 | EN 1529 |  | MEST EN 1529:2010 |
| Persistence between the same climates | EN 1294 | Doors wings EN 1530; doors wings and doors EN 12219 | MEST EN 1294:2009 | MEST EN 1530:2010 |
| Persistence between different climates | EN 1121 | Doors wings EN 1530; Doors wings and doors EN 12219 | MEST EN 1121:2009 | MEST EN 1530:2010 |
| Mechanical characteristics | Hard shock | EN 950 | EN 1192 |  | MEST EN 1192:2009 |
|  | Vertical load | EN 947 | EN 1192 | MEST EN 947:2010 | MEST EN 1192:2009 |
|  | Static buckling | EN 948 | EN 1192 |  | MEST EN 1192:2009 |
|  | Soft shock | EN 949 | EN 1192 |  | MEST EN 1192:2009 |
| General wings alignment | EN 952 | EN 1530 |  | MEST EN 1530:2010 |
| Local wings alignment | EN 952 | EN 1530 |  | MEST EN 1530:2010 |
| Testing the durability of functioning | EN 1191 | EN 12400 | MEST EN 1191:2009 | MEST EN 12400:2009 |
| force handling | EN 12046-2 | EN 12217-2 | MEST EN 12046-2:2009 | MEST EN 12217:2009 |
| thermal isolation | EN ISO 10077 |  |  |  |
|  | EN ISO 12567-1 |  |  |  |
|  | EN ISO 6946 |  |  |  |
| soundproofing | EN 20140-3 | ISO 717-1 |  |  |
| Fire Protection | EN 1634-1 | EN 13501-2 | MEST EN 1634-1:2012 | MEST EN 13501-1:2011 |
| Smoke protection | EN 14013 | EN 14013 |  |  |
| Protection against burglary | ENV 1628 | ENV 1627 |  | MEST EN 1627:2012 |
|  | ENV 1629 |  |  |  |
|  | ENV 1630 |  |  |  |
| Resistance to the explosion | shock tube | EN 13124-1 | EN 13123-1 | MEST EN 13124-1:2009 | MEST EN 13123-1:2009 |
|  | experiment outdoors | EN 13124-2 | EN 13123-2 | MEST EN 13124-2:2009 | MEST EN 13123-2:2009 |
| REVIEW OF STANDARDS FOR ELECTRICAL INSTALLATIONS |
| TECHNICAL REQUIREMENTS | EUROPEAN STANDARDS | NATIONAL STANDARDS |
|  | TESTING METHOD | CLASSIFICATION | TESTING METHOD | CLASSIFICATION |
| Power cables |  | EN 45510-2-8:2004 |  | MEST EN 45510-2-8:2010 |
| reflectors |  | EN 60598-2-5:1998 |  | MEST EN 60598-2-5:2010 |
| Lamps |  | EN 60598-2-25:1994 |  | MEST EN 60598-2-25:2010 |
| switches |  | EN 60947-3:2009 |  | MEST EN 60947-3:2009 |
| REVIEW OF STANDARDS FOR WATER AND SEWAGE MATERIAL |
| TECHNICAL REQUIREMENTS | EUROPEAN STANDARDS | NATIONAL STANDARDS |
|  | TESTING METHOD | CLASSIFICATION | TESTING METHOD | CLASSIFICATION |
| Pipes |  | EN 12201-2:2011 |  | MEST EN 12201-2:2012 |
| Joints |  | EN 12201-3:2011 |  | MEST EN 12201-3:2012 |
| Valves |  | EN 12201-4:2011 |  | MEST EN 12201-4:2012 |
| System for the disposal of waste water (pipes, joints and the system) |  |  |  | MEST EN 1329-1:2011 |

| REVIEW OF STANDARDS FOR THERMAL PANELS |
| --- |
| TECHNICAL REQUIREMENTS | EUROPEAN STANDARDS | NATIONAL STANDARDS |
| Self-supporting isolating sandwich panels with two-sided metal coating | EN 14509 | MEST EN 14509:2010 |
| REVIEW OF STANDARDS FOR INDUSTRIAL FLOOR |
| TECHNICAL REQUIREMENTS | EUROPEAN STANDARDS | NATIONAL STANDARDS |
| Compressive strength | Resin (1:0,9 filled with Sikadur 504 or equivalent) 50N/mm2 (28 days / +23 C) (EN 196-1) |  |
| Flexural Strength | Resin (1:0,9 filled with Sikadur 504 or equivalent) 30N/mm2 (28 days / +23 C) (EN 196-1) |  |

| REVIEW OF STANDADS FOR PAINTS AND COATING SYSTEMS |
| --- |
| TECHNICAL REQUIREMENTS | EUROPEAN STANDARDS | NATIONAL STANDARDS |
|  | TESTING METHOD | CLASSIFICATION | TESTING METHOD | CLASSIFICATION |
| Determination of water permeability |  | EN 1062-3:2008 |  | MEST EN 1062-2:2009 |
| Determination of carbon dioxide permeability |  | EN 1062-6:2002 |  | MEST EN 1062-6:2009 |
| Determination of crack bridging |  | EN 1062-7:2004 |  | MEST EN 1062-7:2009 |

Materials that are not adequate to the type of building that is going to be refurbished must not be used.

All the material must be in line with the Montenegrin legislation.