CLARIFICATIONS

Supply of special vehicle for sewage cleaning and septic tank drainage in the old royal capital Cetinje

Project Identification No. Europaid/131194L/ACT/ME – CRIS No: 2011/274-407/02

| No. | QUESTIONS | ANSWERS |
| --- | --- | --- |
| 1. | Suction hose Top suction hose reel with telescopic arm – Required Directional arm for hose guiding DN100 high pressure hose with ball coupling min 20m concerning that description is related to suction system is this printing mistake? | It is a D100 suction hose with ball coupling, min 20 m. |
| 2. | Vacuum pump Vacuum pump required is rotary blower system which is water cooled. This two requests are in collision because it is impossible to have rotary blower system with water cooling. Please clarify is the requiring vacuum pump with rotary blower system or van pumps (which have water cooling) ? | It is a Rotary blower vacuum pump, cooled. A Rotary vane vacuum pump, cooled, is also acceptable. |
| 3. | Vacuum pump Is it necessary to supply vacuum pump with “rotary blower system” since this could not be water cooled ? | Please, see Answer to question 2. |
| 4. | Top suction hose reel Top suction hose reel with telescopic arm at the page 8 of technical requirement. Is this description related to suction hose reel on the top of vehicle or suction boom on the top of vehicle? | It is description of a suction hose reel on the top of vehicle |
| 5. | Top suction hose reel Should vehicle have top suction hose reel or suction boom on top? | Please, see Answer to question 4. |