- DICTIONARY / Phrase book

for drawings -

| Crnogorski jezik / Montenegrin language | Engleski jezik / English langage |
| --- | --- |
| arhitektura | architecture |
| A-001 |
| Situacija objekta | Situation of the object |
| Regulaciona linija | Regulation line |
| Građevinska linija | Building (engineering) line |
| Glavna garaža | Main garage |
| Trotoar | Sidewalk |
| Kolovoz | Roadway |
| Zeleni pojas | Green area |
| Vrsta projekta | Type of project |
| Glavni projekat | Main project |
| Objekat i lokacija | Object and location |
| Faza projekta | Project phase |
| Broj crteža | Number of drawing |
| Naziv crteža | Title of the drawing |
| Projektant arhitekture | Engineer of architecture |
| Projektant kontrukcije | Structural engineer |
| Projektant vodovoda i kanalizacija | Water supply and sanitation engineer |
| Projektant elektroinstalacija | Engineer of electrical installations |
| A-002 |
| Osnova temelja | Base for foundation-substruction |
| Bunker za smjestaj ogreva | Bunker for fuel wood for housing |
| Prostor kotlarnice | Heating plant room |
| Dimovodni kanal | Chimneys |
| Stepenište za kotlarnicu | Stairs for heating plant (boiler) room |
| A-003 |
| Osnova suterena | The basis of basement |
| Zid od giter bloka | Giter block wall |
| Zid od kartonskih ploča | Wall of cardboard panels |
| Armirani beton | Ferro concrete |
| Dimovodni kanali | Chimneys |
| Bravarske pozicije na fasadi | Locksmith position on the facade |
| Rekapitulacija površina | Recapitulation of the areas |
| Neto površina objekta | Net area of the object |
| Bruto površina objekta | Gross area of the object |
| Legenda površina | Legend of the area |
| Materijal poda | Floor material |
| Materijal zida | Wall material |
| Tehnička prostorija - kotlara | Technical room – boiler room |
| Poludisperzija | Semi-dispersion |
| A-004 |
| Osnova temelja | Base for foundation-substruction |
| Stepenište za kotlarnicu | Stairs for heating plant (boiler) room |
| A-005 |
| Osnova prizemlja | The basis of the ground floor |
| Legenda površina | Legend of the area |
| Glavna garaža | Main garage |
| Pomoćna garaža | Backing garage |
| Tehnička radionica | Technical workshop |
| Servis PP aparata | Service of anti-fire equipment |
| Garderoba | Wardrobe (fiting room) |
| Vertikalna komunikacija | Vertical Communications |
| Toranj za osmatranje | Observation Tower |
| Vjetrobran | Windshield |
| Komandni centar | Command Center |
| Dnevni boravak | Living room |
| Prijem PP aparata | Reception of anti-fire equipment |
| Čajna kuhinja | Kitchenette |
| Mokri čvor | Sanitary knot |
| Soba za odmor ljudstva | Room for the rest of people |
| Hodnik | Corridor |
| Higijena objekta | Hygiene facility |
| Zid od giter bloka | Giter block wall |
| Zid od kartonskih ploča | Wall of cardboard panels |
| Armirani beton | Ferro concrete |
| Dimovodni kanali | Chimneys |
| Zid od sendvič panela | Wall of sandwich panels |
| A-006 |
| Osnova sprata i galerije | The base of the floor and gallerie |
| Vazdušni prostor glavne garaže | Airspace of the main garage |
| Kancelarija zamjenika komandira | Office of the deputy chief |
| Kancelarija sekretarice | Office of secretary |
| Fitness sala | Fitness room |
| Vešeraj | Laundry |
| Parket | parquet |
| Podna keramika | Floor ceramics |
| Prostorija za stoni tennis | Room for table tennis |
| Čelični lim | Steel sheet |
| Materijal poda | Floor material |
| Materijal zida | Wall material |
| A-007 |
| Osnova potkrovlja | The basis of the attic |
| Tavanski prostor | Attic space |
| Zakačka za merdevine | The hook for ladders |
| Platforma od pocinkovanog lima | Platform made ​​of galvanized sheet |
| Trapezasti krovni lim | Trapezoidal sheet metal roof |
| Apartman | Apartment |
| Terasa | Terrace |
| Kosa krovna AB ploča | Leaning roof AB panel |
| Predsoblje | Anteroom |
| Terasa konfrencijske sale | Terrace of the conference hall |
| Akrilni malter | Acrylic mortar |
| Zidna keramika | Wall ceramics |
| A-008 |
| Osnova krovne konstrukcije | The basis of the roof structure |
| Krovna lanterna od čeličnih profila I termopan stakla | The roof lantern of steel bars and thermo glass |
| Krov od čeličnih profila pokriven sendvič krovnim panelom | The roof of steel profiles covered with sandwich roof panel |
| Toranj za osmatranje | Observation tower |
| A-009 |
| Peta fasada krovne ravni | Fifth facade of the roof |
| A-010 |
| Osnova krovne atike tornja | The basis of the tower roof attic |
| A-011 |
| Karakteristični presjek 1-1 | Typical cross-section 1-1 |
| Glava garaža | Main garage |
| Konferencijska sala | Conference hall |
| Prostorija za stoni tenis | Room for table tennis |
| Tavanski prostor | Attic space |
| Servis PP aparata | Service of anti-fire equipment |
| Gips karton ploče | Gypsum board panels |
| Primarni nosač | Primary carrier |
| Sekundarni nosač | Secondary carrier |
| Sendvič panel | Sandwich panel |
| Unutrašnji malter | Internal mortar |
| Giter blok opeka | Giter Brick |
| Demit fasada | Demit facade |
| A-012 |
| Karakteristični presjek 2-2 | Typical cross-section 2-2 |
| Hodnik | Corridor |
| Konferencijska sala | Conference hall |
| Glava garaža | Main garage |
| Stepenište | Stairway |
| Vazdušni prostor stepeništa | Airspace of the stairway |
| Garderoba | Wardrobe |
| Mokri čvor | Sanitary knot |
| Hodnik | Corridor |
| A-013 |
| Fasada A-B | Facade A-B |
| Antenski toranj | Antenna Tower |
| Krovna atika | Roof attic |
| Staklena fasada | Glass facades |
| Sendvič panel | Sandwich panel |
| Krovni sendvič panel | Roof sandwich panel |
| Demit fasada | Demit facade |
| Detalj na fasadi | Detail at the facade |
| Automatska sensor klizna vrata | Automatic sensor sliding-doors |
| A-014 |
| Fasada B-C, D-A | Facade B-C, D-A |
| Staklena fasada | Glass facades |
| Sendvič panel | Sandwich panel |
| Krovni sendvič panel | Roof sandwich panel |
| Demit fasada | Demit facade |
| A-015 |
| Fasada C-D | Façade C-D |
| Demit fasada | Demit facade |
| Sendvič panel | Sandwich panel |
| AA2-2 |
| Krovni sistem | Roof system |
| Insulirani žlijeb nastrešnice | Insulated eaves gutter |
| AA2-1 |
| Krovni sistem | Roof system |
| Vanjski žlijeb | External gutter |
| AA5-1 |
| Krovni sistem | Roof system |
| Zaštita od snijega | Snow guard |
| Atmospheric drainage (NO NUMBER-TABLE NUMBER 18) |
| Atmosferska odvodnja | Atmospheric drainage |
| Trotoar | Sidewalk |
| Kolovoz | Roadway |
| Zeleni pojas | Green area |
| Gradjevinska linija | Building (engineering) line |
| Regulaciona linija | Regulation line |
| Rijeka Lim | River Lim |
| Slivnik | Sink-hole / drain |
| Bunar | Water-well |
| Projected situation (NO NUMBER-TABLE NUMBER 17) |
| Projektovano stanje | Projected situation |
| Kanalizaciona šahta | Sewer coal-pit |
| Spoljnji hidrant | External hydrant |
| CONSTRUCTION |
| steel structure - CONSTRUCTION |
| cross section 1 |
| Nosači | Carriers |
| Razmak | Space |
| Anker ploča | Anker Panel |
| cross section 2 |
| SPECIFICATION |
| Specifikacija čelične konstrukcije | Specification of the steel structure |
| Pod | The floor |
| Gazište | Tread |
| Nosač stuba | Carrier of the pillar |
| Nosač konzola | Carrier of the consoles |
| Nosač lima | Carrier of the sheet metal |
| details of the armature |
| Pos 000 -floor plate garage |
| Podna ploča garaže | Floor plate garage |
| Pos 100 a-plate |
| Gornja zona | Upper zone |
| Donja zona | Lower zone |
| Pos 100-plate |
| Gornja zona | Upper zone |
| Donja zona | Lower zone |
| Pos 107 - beam |
| Grede | Beams |
| Pos 120, 121 |
| Grede | Beams |
| Pos 200-plate upper zone |
| Gornja zona | Upper zone |
| Pos 207, 210, beams |
| Grede | Beams |
| Pos 300, plate |
| Ploča | Plate |
| Gornja zona | Upper zone |
| Donja zona | Lower zone |
| Pos 310, 311, 319, 319 |
| Grede | Beams |
| Anker ploča | Anchor plate |
| Pos 320, 321 - beams |
| Grede | Beams |
| Pos t - foundations |
| Temelji | foundations |
| Pos TP, Z-foundation plate |
| Temeljna ploča | Foundation plate |
| Zidovi podruma | Basement walls |
| Pillars page 3 |
| Stubovi | Pillars |
| Podrum | Basement |
| MECHANICAL INSTALLATIONS |
| Calorifier arrangement for the main garage |
| Calorifier arrangement for ancillary garage |
| Vertical distribution |
| Kancelarija komandira | Office of the chief |
| Kancelarija sekretarice | Office of secretary |
| Kancelarija zamjenika komandira | Office of the deputy chief |
| Mokri čvor | Sanitary knot |
| Hodnik | Corridor |
| Fitness sala | Fitness room |
| Vešeraj | Laundry |
| Prostorija za stoni tennis | Room for table tennis |
| Toranj za posmatranje | Tower for observation |
| Vertikalni razvod mreže | Vertical distribution of the network |
| Vertical distribution 1 |
| Vertikalni razvod mreže | Vertical distribution of the network |
| Vertical distribution 2 |
| Vertikalni razvod mreže | Vertical distribution of the network |
| Building for protection and rescue center, spurt (STRONG CURRENT – HIGH VOLTAGE ) |
| Building for protection and rescue center, spurt(STRONG CURRENT - HIGH VOLTAGE) – THE BASE - Model |
| Osnova temelja, temeljni uzemljivač | The basis of the foundation, foundation earthing |
| Osnova kotlarnice, elektroinstalacije jake struje | The basis of the boiler room, electroinstalation of strong currents |
| Osnova prizemlja, elektroinstalacije jake struje | The base floor, electroinstalation of strong currents |
| Osnova galerije, elektroinstalacije jake struje | The basis of galleries, electroinstalation of strong currents |
| Osnova sprata, elektroinstalacije jake struje | The base floor, electroinstalation of strong currents |
| Vazdušni prostor glavne garaže | Airspace of the main garage |
| Building for protection and rescue center, GRO AND RAZ.TABLE-Model |
| Building for protection and rescue center, weak curRent (LOW VOLTAGE) |
| Building for protection and rescue center, weak curRent (LOW VOLTAGE) - THE BASE - Model |
| Osnova potkrovlja, elektroinstalacije slabe struje | The basis of the attic, a weak electrical current |
| Osnova sprata, elektroinstalacije slabe struje | The base floor, a weak electrical current |
| Vazdušni prostor glavne garaže | Airspace of the main garage |
| Osnova prizemlja, elektroinstalacije slabe struje | The base floor, a weak electrical current |
| Tavanski prostor | Attic space |
| Water Supply and Sewerage |
| Water Supply and Sewerage 1 |
| Sewerage -the basis of gallery |
| Vodovod i kanalizacija | Water Supply and Sewerage |
| Kanalizacija - osnova galerije | Sewage -the basis of gallery |
| Napomena: na svakoj vertikali u sanitarnom čvoru uraditi revizioni fazonski komad | Note: in each vertical of the sanitary facilities to do revision fittings |
| Sewerage -the basis of the ground floor |
| Kanalizacija - osnova prizemlja | Sewage -the basis of ground floor |
| Napomena: na svakoj vertikali u sanitarnom čvoru uraditi revizioni fazonski komad | Note: in each vertical of the sanitary facilities to do revision fittings |
| Vertikalna komunikacija | Vertical communication |
| Ventilacioni ispust | Ventilation outlet |
| Rešetka i kanal za odvod vode sa poda garaže | The grid and a channel to drain water from the floor of the garage |
| Sewerage - the basis of the upper floor |
| Osnova sprata | The basis of the upper floor |
| Vodovod i kanalizacija | Water Supply and Sewerage |
| Napomena: na svakoj vertikali u sanitarnom čvoru uraditi revizioni fazonski komad | Note: in each vertical of the sanitary facilities to do revision fittings |
| Sewage - the base of the foundation |
| Kanalizacija - osnova temelja | Sewage -the base of the foundation |
| Vodovod i kanalizacija | Water Supply and Sewerage |
| Reviziona šahta | Revision shaft |
| Vodomjerna šahta | Water-gauge shaft |
| Stepenište za kotlaru | Stairways for tinker |
| Reviziona šahta (sa duplim poklopcem) | Revision shaft (double cover) |
| Water Supply and Sewerage 2 |
| Kanalizacija – presjek 1-1 | Sewerage – cross section 1-1 |
| Reviziona šahta | Revision shaft |
| Vodovod i kanalizacija | Water Supply and Sewerage |
| Ventilacioni ispust | Ventilation outlet |
| Ventilaciona kapa | Ventilation cap |
| Water Supply and Sewerage 3 |
| Vodovod – izometrija | Water supply system - isometry |
| Projekat vodovoda – izometrija | Project of the water supply system - isometry |
| Unutrašnja mreža (voda za piće) | Internal network (drinking water) |
| Proračun gubitka pritiska u cijevima | Calculation of pressure loss in pipes |
| Dionica | Section |
| Količina vode | The amount of water |
| Prečnik | Diameter |
| Brzina vode | Velocity of water |
| Jedinični gubitak | Unit loss |
| Dužina cijevi | Pipe length |
| Ukupni gubitak | Total loss |
| Gubitak u mreži | The loss in the network |
| Geodetksa visina | Geodetic height |
| Gubitak u vodomjeru | Loss in the water-gauge |
| Bunar | Water -well |
| Etaža I i II | Floor I and II |
| Prizemlje | Ground floor |
| Lavabo | Sink |
| Pisoar | Urinal |
| Kada | Tub |
| Sudoprea | Kitchen sink |
| Česma | Fountain |
| Trokadera | Trocadero |
| Hidrantska mreža | Hydrants network |
| Proračun gubitka pritiska u cijevima | Calculation of pressure loss in pipes |
| Dionica | Section |
| Količina vode | The amount of water |
| Prečnik | Diameter |
| Brzina vode | Velocity of water |
| Jedinični gubitak | Unit loss |
| Dužina cijevi | Pipe length |
| Gubitak u mreži | The loss in the network |
| Geodetksa visina | Geodetic height |
| Minimalni pritisak na mlaznice | Minimum pressure on the jets |
| Gubitak u vodomjeru | Loss in the water-gauge |
| Ukupni gubici | Total losses |
| WATER SUPPLY SYSTEM -THE BASIS OF THE GROUND FLOOR |
| Vodovod – osnova prizemlja | Water supply system – the basis of the ground floor |
| Hidrantska mreža | Hydrants network |
| Unutrašnja mreža (voda za piće) | Internal network (drinking water) |
| Vodomjerna šahta | Water-gauge shaft |
| Rešetka i kanal za odvod vode sa poda garaže | The grid and a channel to drain water from the floor of the garage |
| Pad u podu | Decline in the floor |
| WATER SUPPLY SYSTEM -THE BASIS OF THE UPPER FLOOR |
| Vodovod – osnova sprata | Water supply system – the basis of the upper floor |
| WATER SUPPLY SYSTEM -THE BASIS OF THE GALLERY |
| Vodovod – osnova galerije | Water supply system – the basis of the gallery |
| SITUATION-THE BASIS OF THE GROUND FLOOR |
| Situacija – osnova prizemlja | Situation – the bass of the ground floor |
| Hidrantska mreža | Hydrants network |
| Unutrašnja mreža (voda za piće) | Internal network (drinking water) |
| Vodomjerna šahta | Water-gauge shaft |
| Reviziona šahta | Revision shaft |
| Rešetka i kanal za odvod vode sa poda garaže | The grid and a channel to drain water from the floor of the garage |
| Vertikalna komunikacija | Vertical communication |